## Slide 1
CCoommppuutterer FFununddaammenenttaallss:: PPrradadeeepep KK.. SSiinhanha && PPrriititi SSiinhanha
Ref Page Chapter 3: Number Systems Slide 1/40

## Slide 2: Learning Objectives
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
In this chapter you will learn about:
Non-positional number system
Positional number system
Decimal number system
Binary number system
Octal number system
Hexadecimal number system
Ref Page 20
(Continued on next slide)

## Slide 3: Learning Objectives
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
Ref Page 20
(Continued from previous slide..)
Convert a number’s base
  Another base to decimal base
  Decimal base to another base
  Some base to another base
Shortcut methods for converting
  Binary to octal number
  Octal to binary number
  Binary to hexadecimal number
  Hexadecimal to binary number
Fractional numbers in binary number system

## Slide 4: NNuummber Systems
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
Two types of number systems are:
Non-positional number systems
Positional number systems
Ref Page 20

## Slide 5: Non-positional Number Systems
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
Characteristics
  Use symbols such as I for 1, II for 2, III for 3, IIII for 4, IIIII for 5, etc
  Each symbol represents the same value regardless of its position in the number
  The symbols are simply added to find out the value of a particular number
Difficulty
  It is difficult to perform arithmetic with such a number system
Ref Page 20

## Slide 6: Positional Number Systems
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
Characteristics
  Use only a few symbols called digits
  These symbols represent different values depending on the position they occupy in the number
Ref Page 20
(Continued on next slide)

## Slide 7: Positional Number Systems
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
Ref Page 21
(Continued from previous slide..)
The value of each digit is determined by:
  The digit itself
  The position of the digit in the number
  The base of the number system
(base = total number of digits in the number system)
The maximum value of a single digit is always equal to one less than the value of the base

## Slide 8: Decimal Number System
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
Characteristics
A positional number system
 Has 10 symbols or digits (0, 1, 2, 3, 4, 5, 6, 7,
8, 9). Hence, its base = 10
The maximum value of a single digit is 9 (one less than the value of the base)
Each position of a digit represents a specific power of the base (10)
We use this number system in our day-to-day life
Ref Page 21
(Continued on next slide)

## Slide 9: Decimal Number System
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
Ref Page 21
(Continued from previous slide..)
Example
258610 = (2 x 103) + (5 x 102) + (8 x 101) + (6 x 100)
= 2000 + 500 + 80 + 6

## Slide 10: BBiinary Number System
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
Characteristics
Ref Page 21
Hence its
A positional number system
Has only 2 symbols or digits (0 and 1). base = 2
The maximum value of a single digit is 1 (one less than the value of the base)
Each position of a digit represents a specific power of the base (2)
This number system is used in computers
(Continued on next slide)

## Slide 11: BBiinary Number System
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
Ref Page 21
(Continued from previous slide..)
Example
101012 = (1 x 24) + (0 x 23) + (1 x 22) + (0 x 21) x (1 x 20)
= 16 + 0 + 4 + 0 + 1
= 2110

## Slide 12: Representing Numbers in Different Number Systems
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
In order to be specific about which number system we are referring to, it is a common practice to indicate the base as a subscript. Thus, we write:
101012 = 2110
Ref Page 21

## Slide 13
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
Bit
Bit stands for binary digit
A bit in computer terminology means either a 0 or a 1
A binary number consisting of n bits is called an n-bit number
Ref Page 22

## Slide 14: Octal Number System
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
Characteristics
A positional number system
Has total 8 symbols or digits (0, 1, 2, 3, 4, 5, 6, 7). Hence, its base = 8
The maximum value of a single digit is 7 (one less than the value of the base
Each position of a digit represents a specific power of the base (8)
Ref Page 22
(Continued on next slide)

## Slide 15: Octal Number System
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
20578
Ref Page 22
= (2 x 83) + (0 x 82) + (5 x 81) + (7 x 80)
= 1024 + 0 + 40 + 7
= 107110
(Continued from previous slide..)
Since there are only 8 digits, 3 bits (23 = 8) are sufficient to represent any octal number in binary
Example

## Slide 16: HHeexadecimal Number System
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
Characteristics
A positional number system
Has total 16 symbols or digits (0, 1, 2, 3, 4, 5, 6, 7, 8, 9, A, B, C, D, E, F). Hence its base = 16
The symbols A, B, C, D, E and F represent the decimal values 10, 11, 12, 13, 14 and 15 respectively
The maximum value of a single digit is 15 (one less than the value of the base)
Ref Page 22
(Continued on next slide)

## Slide 17: HHeexadecimal Number System
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
1AF16
Ref Page 22
= (1 x 162) + (A x 161) + (F x 160)
= 1 x 256 + 10 x 16 + 15 x 1
= 256 + 160 + 15
= 43110
(Continued from previous slide..)
Each position of a digit represents a specific power of the base (16)
Since there are only 16 digits, 4 bits (24 = 16) are sufficient to represent any hexadecimal number in binary
Example

## Slide 18: Converting a Number of Another Base to a Decimal Number
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
Method
Step 1:
Ref Page 23
Determine the column (positional) value of each digit
Step 2:
Multiply the obtained column values by the digits in the corresponding columns
Step 3:
Calculate the sum of these products
(Continued on next slide)

## Slide 19: Converting a Number of Another Base to a Decimal Number
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
47068 = 4 x 83 + 7 x 82 + 0 x 81 + 6 x 80
= 4 x 512 + 7 x 64 + 0 + 6 x 1
= 2048 + 448 + 0 + 6
= 250210
Example
47068 = ?10
Common values multiplied by the
corresponding digits
Sum of these products
(Continued from previous slide..)
Ref Page 23

## Slide 20: Converting a Decimal Number to a Number of Another Base
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
Division-Remainder Method
Ref Page 25
Step 1:
Divide the decimal number to be converted by the value of the new base
Step | 2: | Record the remainder | from Step 1 as | the
 |  | rightmost digit (least | significant digit) of | the
new base number
Step 3:
Divide the quotient of the previous divide by the new base
(Continued on next slide)

## Slide 21: Converting a Decimal Number to a Number of Another Base (Continued from previous slide..)
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
Step 4:
Ref Page 25
Record the remainder from Step 3 as the next digit (to the left) of the new base number
Repeat Steps 3 and 4, recording remainders from right to left, until the quotient becomes zero in Step 3
Note that the last remainder thus obtained will be the most significant digit (MSD) of the new base number
(Continued on next slide)

## Slide 22: Converting a Decimal Number to a Number of Another Base
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
8 | 952 | Remainder
 | 119 | s 0
 | 14 | 7
 | 1 | 6
 | 0 | 1
Ref Page 26
Hence, 95210 = 16708
(Continued from previous slide..)
Example
95210 = ?8
Solution:

## Slide 23: Converting a Number of Some Base to a Number of Another Base
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
Method
Ref Page 27
Step
number
to a decimal
1: Convert the original number (base 10)
Step 2:
Convert the decimal number so obtained to the new base number
(Continued on next slide)

## Slide 24: Converting a Number of Some Base of Another Base
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
(Continued from previous slide..)
Example
5456 = ?4
Solution:
Step 1: Convert from base 6 to base 10
5456 = 5 x 62 + 4 x 61 + 5 x 60
= 5 x 36 + 4 x 6 + 5 x 1
= 180 + 24 + 5
= 20910
Ref Page 27
(Continued on next slide)
to a Number

## Slide 25: Converting a Number of Some Base of Another Base
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
Step 2:
Convert 20910 to base 4
Hence, 20910 = 31014
So, 5456 = 20910 = 31014
Thus, 5456 = 31014
52
13
3
0
Ref Page 28
Remainders
1
0
1
3
4 209
(Continued from previous slide..)
to a Number

## Slide 26: Shortcut Method for Converting a Binary Number to its Equivalent Octal Number
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
Method
Step 1:
Ref Page 29
Divide the digits into groups of three starting from the right
Step 2:
Convert each group of three binary digits to one octal digit using the method of binary to decimal conversion
(Continued on next slide)

## Slide 27: Shortcut Method for Converting a Binary Number to its Equivalent Octal Number
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
Step 1:
Ref Page 29
Step 2:
Divide the binary digits into groups of 3 starting from right
001 101 010
Convert each group into one octal digit
0012 = 0 x 22 + 0 x 21 + 1 x 20 = 1
1012 = 1 x 22 + 0 x 21 + 1 x 20 = 5
0102 = 0 x 22 + 1 x 21 + 0 x 20 = 2
Hence, 11010102 = 1528
(Continued from previous slide..)
Example
11010102 = ?8

## Slide 28: Shortcut Method for Converting an Octal Number to Its Equivalent Binary Number
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
Method
Step 1:
Ref Page 30
Convert each octal digit to a 3 digit binary number (the octal digits may be treated as decimal for this conversion)
Step
binary single
groups binary
2: Combine all the resulting (of 3 digits each) into a number
(Continued on next slide)

## Slide 29: Shortcut Method for Converting an Octal Number to Its Equivalent Binary Number
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
Step 1:
Ref Page 30
Step 2:
Convert each octal digit to 3 binary digits 58 = 1012, 68 = 1102, 28 = 0102
Combine the binary groups
5628 | = 101 | 110 | 010
 | 5 | 6 | 2
Hence, 5628 = 1011100102
(Continued from previous slide..)
Example
5628 = ?2

## Slide 30: Shortcut Method for Converting a Binary Number to its Equivalent Hexadecimal Number
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
Method
Ref Page 30
Step 1:
Step 2:
Divide the binary digits into groups of four starting from the right
Combine each group of four binary digits to one hexadecimal digit
(Continued on next slide)

## Slide 31: Shortcut Method for Converting a Binary Number to its Equivalent Hexadecimal Number
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
Step 1:
Ref Page 31
Divide the binary digits into groups of four starting from the right
Step 2:
0011 1101
Convert each group into a hexadecimal digit
00112 = 0 x 23 + 0 x 22 + 1 x 21 + 1 x 20 = 310 = 316
11012 = 1 x 23 + 1 x 22 + 0 x 21 + 1 x 20 = 310 = D16
Hence, 1111012 = 3D16
(Continued from previous slide..)
Example
1111012 = ?16

## Slide 32: Shortcut Method for Converting a Hexadecimal Number to its Equivalent Binary Number
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
Method
Step 1: Convert the decimal equivalent of each hexadecimal digit to a 4 digit binary number
Step 2: Combine all the resulting binary groups
(of 4 digits each) in a single binary number
Ref Page 31
(Continued on next slide)

## Slide 33: Shortcut Method for Converting a Hexadecimal Number to its Equivalent Binary Number
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
216 =
Ref Page 32
210
= 00102
A16 = 1010 = 10102
B16 = 1110 = 10112
(Continued from previous slide..)
Example
2AB16 = ?2
Step 1: Convert each hexadecimal digit to a 4 digit binary number

## Slide 34: Shortcut Method for Converting a Hexadecimal Number to its Equivalent Binary Number (Continued from previous slide..)
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
Step 2: Combine the binary groups
Ref Page 32
2AB16 = 0010 | 1010 | 1011
2 | A | B
Hence, 2AB16 = 0010101010112

## Slide 35: Fractional Numbers
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
Ref Page 33
Fractional numbers are formed same way as decimal number system
In general, a number in a number system with base b
would be written as:
an an-1… a0 . a-1 a-2 … a-m
And would be interpreted to mean:
an x bn + an-1 x bn-1 + … + a0 x b0 + a-1 x b-1 + a-2 x b-2 +
… + a-m x b-m
The symbols an,
an-1, a-m
…, in above representation
should be one of the b symbols allowed in the number system

## Slide 36: Formation of Fractional Numbers in Binary Number System (Example)
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
Position
Position Value
4 | 3 | 2 | 1 | 0 | . -1 | -2 | -3 | -4
24 | 23 | 22 | 21 | 20 | 2-1 | 2-2 | 2-3 | 2-4
16 8
4
2
1
1/2 1/4 1/8
1/16
Quantity Represented
Binary Point
(Continued on next slide)
Ref Page 33

## Slide 37: Formation of Fractional Numbers in Binary Number System (Example) (Continued from previous slide..)
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
Example
Ref Page 33
110.1012
= 1 x 22 + 1 x 21 + 0 x 20 + 1 x 2-1 + 0 x 2-2 + 1 x 2-3
= 4 + 2 + 0 + 0.5 + 0 + 0.125
= 6.62510

## Slide 38: Formation of Fractional Numbers in Octal Number System (Example)
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
Position
3
2 1 0 . -1 -2
-3
Position Value
83
82 81 80
8-1
8-2
8-3
512 64
8
1
1/8
1/64
1/512
Quantity Represented
Octal Point
Ref Page 33
(Continued on next slide)

## Slide 39: Formation of Fractional Numbers in Octal Number System (Example)
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
(Continued from previous slide..)
Example
127.548 = 1 x 82 + 2 x 81 + 7 x 80 + 5 x 8-1 + 4 x 8-2
= 64 + 16 + 7 + 5/8 + 4/64
= 87 + 0.625 + 0.0625
= 87.687510
Ref Page 33

## Slide 40: Key Words/Phrases
Computer Fundamentals: Pradeep K. Sinha & Priti Sinha
Ref Page 34
Base
Binary number system
Binary point
Bit
Decimal number system
Division-Remainder technique
Fractional numbers
Hexadecimal number system
Least Significant Digit (LSD)
Memory dump
Most Significant Digit (MSD)
Non-positional number system
Number system
Octal number system
Positional number system